Fifthwheel Departure Checklist

by David Tarnoff

# Text boxes

Hitching

 Tow vehicle mirrors adjusted

 Lower truck tailgate

 Preflight hitch

 Back truck up to hitch

 Adjust hitch height to pickup

 Stow 120VAC cord

 Extract hitch lock bar handle

 Back truck under kingpin until hitch engages

 Visually check kingpin lock bar

 Raise landing gear ½ inch

 Perform tug test

 Connect umbilical cord & breakaway switch cable

 Raise truck tailgate

 Fully retract landing gear

 Remove trailer wheel chocks

 Lock front basement door

 Verify trailer lights

 Verify landing gear, stabilizers, & tailgate

 Set transmission to Tow/Haul

 Verify brake controller lights.

Close wardrobe doors

Close windows

Close vent

Lower antenna

Turn off booster

Secure television

Secure towel rack

Secure toiletries

Secure shower door

Secure cabinet doors

Close vent

Close bathroom door

Sliding door secured

Light off

All lights off

Light off

Secure chairs

Radio off

Television secured

Surge protector off

Drawers secured

Desk chair stowed

Garbage taken out

Microwave turntable

Close vent

Turn off HVAC

Close cabinets

Close windows

Close windows

Turn off lights

Turn off light

Lights, pump, & htr off

Turn off water heater

Refer door shut

Refer on if using gas

Retract rear stabilizers/stow pads

Check slide roofs

Retract slides w/door open

Close and lock door

Stow handle

Stow stairs

Store ladder, rugs, and stabilizer wrench

Turn off LP if no fridge

Awning stowed & locked

Grease K.P. & attach Teflon disk

Verify sewer, city water, and cable caps are connected

Lock side basement doors

Close front basement door

 Dump tanks/prime black tank	 Verify tire pressure: 65 psi except truck rear: 75 psi

 Fill fresh water tank if needed	 Tighten lug nuts

Shore hoses and TV cable

1

2

3